## Slide 1: United States Forest Service Fire & Aviation Management
Safety First as a Core Value

## Slide 2: Firefighter Training, S-130
Introduction to Fire fighting

## Slide 4: Course Objectives
Construct fire line to required standards, using various methods for construction.
Strengthen, reinforce and use holding actions on the fire line.
Extinguish the fire with or without the use of water.
Locate yourself and the fire on a map

## Slide 5: Objectives (continued)
Assess and report fire situation data (written or oral) by radio and/or messenger.
Complete assigned tasks in a safe and efficient manner.
Given and assignment in a wildfire environment, describe factors in that environment which could impact safety.

## Slide 6: Safety
Safety is defined as freedom from exposure to danger.

## Slide 7: Fire fighters’ Requirements
Knowledge and skill in methods of avoiding accidents, injury and exposure to danger.
An ability and attitude that grows with experience and training.
Fire fighting personnel must use the knowledge and skills gained through training and experience in all situations.

## Slide 8: Safety Rules
LCES - Lookouts, Communications, Escape Routes and Safety Zones
The 18 Situations that Shout Watch Out
The Ten Standard Fire Orders

## Slide 10: Fire Orders
Fight fire aggressively but provide for safety first
Initiate all actions based on current and expected fire behavior
Recognize current weather conditions and obtain weather forecasts
Ensure instructions are given and understood
Obtain current information on fire status
Remain in communication with crew members, your supervisor and adjoining forces
Determine safety zones and escape routes
Establish lookouts in potentially hazardous situations
Retain control at all times
Stay alert, keep calm, think clearly and act decisively

## Slide 13: Types of Hazards
Subjective Hazards: are hazards that we have direct control over.
  Example: condition of equipment, the decision to turn your back.
Objective Hazards: are hazards that we have no control over.
  Lightning
  Fire weakened timber
  Rolling rocks, logs
  Entrapment by fire

## Slide 19: Environmental Hazards
Heat stress
Hypothermia
Darkness
Carbon monoxide
Dust

## Slide 22: Biological Hazards
Snakes
Insects (bees, ticks, etc.)
Animals (bears, moose, etc.)
Plants (poison oak, ivy, cactus, etc.)
Microorganisms (giardia)
Viral infections (colds, influenza, etc.)

## Slide 24: Equipment Hazards
Cuts (saws, tools, etc.)
Burns from mufflers (pumps, saws, etc.)
Noise (hearing impairment levels)
Foreign objects thrown from moving parts
Hand tools (pulaski, shovel, etc.)
Dozers, tractors/plows, etc.)

## Slide 25: Aircraft (rotor and fixed wing) Hazards
Retardant drops
Bucket drops
Sling loads
Helicopter rotor wash breaking trees and snags (tops, branches, limbs, etc.)
Transport of personnel

## Slide 28: Fire Environment Hazards
The actual fire (running, smoldering, creeping)
Burns
Smoke
Unexpected or erratic winds
Darkness
Falling snags

## Slide 29: Base/Camp Related Hazards
Sleeping areas
Sanitation
Maintaining personal hygiene
Food

## Slide 30: Hazards Trees and Snags
Living
Dying (still alive, but with little or no chance of recovery)
Dead (snags)

## Slide 32: Working in Unsafe Areas
Do not enter the area until it is safe
Make the area safe to work in.
  Fall snags and hazard trees
  Identify the hazard
  Provide a safe area
  Communicate hazards to supervisor and adjoining forces
Provided you have received approval from your supervisor and you are qualified.

## Slide 33: Firefighter Preparedness
Personal gear
Care and maintenance of personal gear
Accountability
Cleanliness and organization

## Slide 34: Weight Limits

## Slide 35: Personal Protective Equipment (PPE)
Hard hat
Eye protection
Hearing protection
Gloves
Flame resistant clothing - Nomex
Leather lace up work boots, 8 inch high
Socks

## Slide 36: Personal Protective Equipment (PPE)
Fire shelters are required
Canteens are for drinking water
Headlamps

## Slide 37: Personal Items
Eyeglasses
Jacket or Coat, Sweatshirt
Cotton under ware
Socks good quality
Personal hygienic gear
  foot powder
  tooth brush and paste
Rain gear

## Slide 38: Problems associated with large wildfires
Too many people were reporting to one supervisor
Different emergency response structures
Lack of any structure for coordinated planning between agencies
Unclear lines of authority
Terminology differences between agencies
Unclear or unspecified incident objectives
Inadequate and incompatible communication systems

## Slide 40: The Incident Command System
Span of control
Standard use of terminology
Consolidated use of action plans
Integrated communications
Predesignated incident facilities
Comprehensive resource management

## Slide 41: Types of Crews
Organized Type I and II crews must be 18-20 persons.
Hand crews are usually used to construct fire line with cutting tools, scraping tools, smothering tools and chain saws.
Hand crews are also used to assist in making hose lays.

## Slide 42: Type I Crews
Interagency Hotshot/Hotshot Crews
18-20 person smoke jumper crew
Are a national resource
Funded by fire management and is primary job

## Slide 46: Type II Crews
Snake River Valley (SRV)
Southwest Firefighters (SWFF)
Montana Indian Fire fighters (MIFF)
Inmates
Agency Regulars
Alaskan Native
Job Corps
Emergency Hires (EFF)(CWN)(Blue card)

## Slide 47: Engine Crews

## Slide 51: Helicopters

## Slide 58: Common Problems Associated With Various Fire Crews
Safety practices and attitudes
Lack of training and experience
Off-shift showering etc.
Tools and equipment left on the fire line
Fatigue factors
Crew Morale
Security

## Slide 61: Transportation of Personnel and Tools Hazards Foot Travel
Whipping branches
Rolling rock or logs
Vehicles, tractors and ATV’s
Unstable footing
Stream or canal crossings
  Avoid high log crossing
  Watch the log not the water
  In swift current face the stream, remove boots, loosen pack

## Slide 62: Transportation of Personnel and Tools Hazards Foot Travel
Stump holes
  Avoid root holes from upended trees
  Watch out for burned stumps that may be hidden under ash layer
  Beware of white ash that may indicate stump hole (test with stick or hand tool)
Locate hazards (poisonous insects, snakes or plants; polluted water

## Slide 63: Firing Devices Objectives
Describe two hazards to operators when using a fusee
Given a fusee demonstrate or simulate how to ignite, use and extinguish

## Slide 66: Water Use Hose Lays
Simple hose lays
Progressive hose lays

## Slide 67: Water Use Water Patterns
Straight stream
  Too hot to get too close
  The fire is confined to a small area
  A lot of pressure is needed to reach any distance
  Targets cannot be reached with fog

## Slide 68: Water Use Water Patterns
Fog
  Needed for close work
  Fire covers a larger area
  A smaller volume of water is required to put the fire out
  Fog patterns may be used when hot spotting, building wet line, direct attack and mop-up
  Fog patterns provides the most personal protection

## Slide 69: Water Use Water Applications
If fire is hot use straight steam to knock the flames down (if fog/spray will not work)
Direct the fog spray parallel to the edge at the base of the flames
Once on the edge continue with a fog pattern
Be sure fire is knocked down well before going further

## Slide 70: Water Use Water Applications
Watch the extinguished edge and behind in case of flare-ups
Follow up wet line with hand line as soon as possible, especially in heavy fuels
Aim accurately and maintain water stream in a sweeping motion
Apply water intermittently
  Conserves water
  Determines if more water is needed

## Slide 71: Suppression Objectives
Name parts of a fire
Describe three methods of attack
Describe four kinds of fire control line
Describe black line concept
Describe three methods for breaking the fire triangle

## Slide 72: Suppression Objectives
Describe five fire behavior terms
Name four hazards to an existing control line when burning inside the fire line
Describe the proper follow-up procedure for a tractor plow fire line for fire line personnel
Describe two kinds of coordinated crew techniques used for fire line construction

## Slide 73: Suppression Objectives
Describe safety procedures to follow when in an area where retardant/water drops are being made
Describe five safety procedures to follow when working around dozers, tractor plows and engines

## Slide 74: Suppression Parts of a Fire
Head
Finger
Flank
Rear
Perimeter
Island
Pocket

## Slide 75: Suppression Parts of a Fire
Origin
Anchor point
Spot fires

## Slide 76: Suppression Methods of Attack
Direct attack
Indirect attack
Parallel attack

## Slide 77: Suppression Black-line Concept
The only safe line is a black line
Fuels that remain between the main fire and the control line are burned out, or allowed to burn to the control line
This method ensures that fuels and heat remain inside the control line and prevents the fire from making a run at the control line

## Slide 78: Suppression Type of Fire Control Line
Constructed fire line
  Hand line
  Machine line
  Wet line
  Retardant line
  Detonation line

## Slide 79: Suppression Type of Fire Control Line
Natural control line
  Cold fire edge
  Fuel break
    Streams, lakes, ponds, rock slides and areas of sparse fuels
  Previously constructed barriers
    Roads, canals, etc.

## Slide 80: Suppression The Fire Triangle
Fuel - any combustible material
Oxygen - in the air
Heat - a source of ignition

## Slide 81: Suppression Methods for Breaking the Fire Triangle
Fuel - Separate the fuel to prevent combustion or remove fuel during fire line construction
Oxygen - Suffocate the fire with dirt or water to rob the fire of oxygen
Heat - Cool the fire by applying water, dirt, retardant or a combination

## Slide 82: Suppression Fire Line Construction Standards
Fuel type
Fuel moisture
Continuity and arrangement
Temperatures
Increases in wind

## Slide 83: Suppression Fire Line Construction Standards
Fuel type
  Forest
  Desert
  Tundra
Fuel moisture
  The lower the fuel moisture the greater the chances for combustion and fire spread

## Slide 84: Suppression Fire Line Construction Standards
Continuity and arrangement
  The closer and more continuous the fuels, both horizontally and vertically, the greater the chance for combustion and fire spread (heavy fuel loading, ladder fuels)

## Slide 85: Suppression Fire Line Construction Standards
Temperatures
  Will inversely effect the fuel moisture
  The higher the temperature the lower the fuel moisture
  As fires burn more intensely, more heat is produced and combustion and fire spread increases

## Slide 86: Suppression Fire Line Construction Standards
Wind
  Increases in wind will increase the amount of oxygen available, increasing the chances for combustion, spotting and fire spread

## Slide 87: Suppression Fire Behavior Description
Smoldering
Creeping
Running
Spotting
Crowning

## Slide 88: Suppression Threats to Existing Control Lines
Spotting
Rolling debris
Creeping
Radiant heat

## Slide 89: Suppression Tractor Fire Line Procedures
Clean-up
Break-machine pile and berms
Fireproof needed areas
Prepare and burn out control line
Limb up trees
Snags that threaten control lines
Mop-up interior
Patrol control lines

## Slide 90: Suppression Coordinated Crew Techniques
Progressive line construction
  Bump-up
  One-lick
  Wedge
  Reverse wedge
Leap frog method

## Slide 91: Suppression Retardant/Water Drop Safety Procedures
Move back into the area quickly to take advantage of retardant
Remember that the area may be slick after retardant drops

## Slide 92: Suppression Retardant/Water Drop Safety Procedures
Lie down facing oncoming aircraft
  Helmet on with chinstrap, feet spread, goggles in place
Hold hand tool at side
  Grab something solid
    Rock
    Tree
    Shrub

## Slide 93: Suppression Retardant/Water Drop Safety Procedures
After initial drop move out of the area until you have received assurance that no more drops are to be made in the area

## Slide 94: Suppression Safety Procedures Used Around Fire line Equipment - Engines
Be alert when engine is moving
Be alert to hazards of a charged hose line
Nozzle operators and personnel nearby must wear eye protection
Be alert and on the lookout for rolling materials when working uphill or downhill of equipment

## Slide 95: Suppression Safety Procedures Used Around Fire line Equipment - Tractors
Be alert to moving equipment
Tractors always have the right-of-way
Maintain 50 foot minimum distance
Be careful and maintain stable footing when working around winch cables
Work a safe distance away depending on fuels and terrain

## Slide 96: Suppression Safety Procedures Used Around Fire line Equipment - Tractors
Do not assume the operator knows where you are
Be alert to night operations
Do not sleep on the fire line

## Slide 97: Suppression Securing the Control Line Objectives
Describe how each of the four senses aid in detecting burning materials
Discuss the importance of breaking up and dispersing accumulations of fuel adjacent to the fire line
Demonstrate the technique of cold-trailing

## Slide 98: Suppression Securing the Control Line Objectives
Given a constructed control-line, strengthen the line to facilitate holding by rearranging and fireproofing fuels adjacent to fire-line
State three factors that determine the amount of additional work required for a water or retardant line

## Slide 99: Suppression Methods of Mop-up
Dry mop-up
  Scraping
  Digging
  Stirring
  Mixing
  Separating
  Turning logs

## Slide 100: Suppression Methods of Mop-up
Wet Mop-up (water application)
  Apply in fine spray
  Apply from control line towards the inside of the burn
  Apply from outside the burn area inwards to the center of the burned area
  Use straight stream to penetrate or reach a target (begin from the base of the tree and work to the top of the tree)

## Slide 101: Suppression Methods of Mop-up
Wet Mop-up
Use hand tools in combination with soil and water
  Scraping
  Digging
  Stirring Mixing
  Separating

## Slide 102: Suppression Mop-up - Hazards in the General Area
Overhanging trees
Snags
Leaning trees (leaners)
Branches, tree tops, loose tree bark
Hanging trees
Trees with roots burned away
Cat faced trees

## Slide 103: Suppression Mop-up - Hazards Associated with Water Use
Hot rocks
White ash
Fire pits
Ground fire
Rock and dirt particles
Be aware not only of yourself, but for those working around you.

## Slide 104: Suppression Systematic Mop-up
Start with the hottest area and progress toward the coolest
Plan a beginning and ending point
Work inward from the control line
Examine the entire assigned area
Make sure instructions are clear. Ask questions???

## Slide 105: Suppression Using the Four Senses - Mop-up
Sight
  Smoke - Look up as well as down. A treetop may be on fire
  Heat waves
  Steam
  White ash - White ash indicates heat and burning, the ash may be covering hot embers
  Stump holes

## Slide 106: Suppression Using the Four Senses - Mop-up
Sight
  Gnats - Gnats often hover over hot spots
  Select an advantageous spot to rest to observe for signs of hot spots
  Look facing into the sun in shaded areas to see small smokes

## Slide 107: Suppression Using the Four Senses - Mop-up
Touch
  Do not wear gloves
  At first, feel about 1 inch away using the back or the hand, then carefully with direct contact

## Slide 108: Suppression Using the Four Senses - Mop-up
Smell
  Smoke
  Burning materials and gases that these materials give off

## Slide 109: Suppression Using the Four Senses - Mop-up
Hearing - listen for the:
Crack and pop of burning materials
Hiss when water touches hot materials

## Slide 110: Suppression Mop-up
Patrol along control lines to check for spot fires and heat to prevent escaping. Patrol both sides of the control line.

## Slide 111: Suppression Reinforce Treated Areas - Mop-up
Construct fire line
Limb up nearby trees and brush
Fireproof fuels outside the control
Have snags fallen